## Slide 1
Course Info
Time: TR 11:10-12:25 AM
M 3:00-3:50 PM
Location: CHEN 106
Instructor: Dr. Martin Sentmanat
Office: CHEN 248
Phone: (979) 862-7687
Email: martin.sentmant@tamu.edu
Office Hours
  M 10:00-11:00 AM
  W 1:00-3:00 PM
Category | Date | Percentage
Homework | N/A | 10%
Daily Quizzes | N/A | 10%
Midterm 1 | Sep 27th | 25%
Midterm 2 | Nov 13th | 25%
Final | Dec 6th 8:00-10:00 | 30%

## Slide 3
Review
Mass (m) and mass flow ()
Volume and volumetric flow ()
In this course, Q is volumetric flow, not heat
Density ()
  Changes inversely with temperature due to increases in volume
Weight
  Heaviness of an object, downward force due to gravity
Force ()
  An action that has direction or maintains the motion of an object
  Converting between force and mass is always accompanied by , a conversion factor ()
    For the SI system of units, this just happens to be
Vectors ()
  A quantity having a magnitude and direction
  Can be split into components
  Magnitude of vectors can be found by:
Velocity ()
Acceleration ()
Momentum ()
  Linear Momentum can be used to find force:
Energy (scalar)
  Kinetic energy ()
  Potential energy ()

## Slide 4
Introduction
What is a fluid?
You can classify something as a fluid or non-fluid based on how it reacts to a shear force (A force acting parallel to the surface)
  Non-fluids can resist shear forces (solids)
  Fluids deform under a shear force (liquids and gases)
States of Matter
Solids: have a lattice structure that holds them together, making them not deform
Liquids: held together by weaker forces, the forces are dependent on the separation distance of the molecules
Gases: spread far apart and have very weak interactions
  Molecules collide with each other
  Will not tend to fall when “poured” out of a cup
Modulus of elasticity tells how stiff something is
Kinematic viscosity is viscosity normalized by density (viscosity/density)
Force Conversion:
Mass Conversion: M

## Slide 5
Some other common units are and , which are units of force that are normalized so that the weight of 1 kg is 1
Unit system | value
SI (scientific) | 
SI (engineering) | 
CGS (scientific) | 
CGS (engineering) | 
English Engineering | 
English Absolute | 
British Gravitational | 
Unit system | 
SI (scientific) | 
SI (engineering) | 
CGS (scientific) | 
CGS (engineering) | 
English Engineering | 
English Absolute | 
British Gravitational | 

## Slide 6
Basic Laws of Fluid Flows
Conservation of Mass
Conservation of Energy – 1st Thermo
Conservation of Momentum – 2nd Newton
Fluid Properties
Density/ (Mass/Volume)
  We usually assume this is constant for liquids (incompressible)
  EX densities: Water - 1000 Mercury 13,588 Hydrogen 0.083
Pressure/P (Force/Area)
  Type of stress
  Atmospheric Pressure ()
  Guage Pressure ()
    Pressure above atmospheric
    Negative gauge pressures are referred to as a vacuum
  Absolute Pressure ()
Temperature
  Relates to internal energy
These Properties can be related to each other through equations of state
  EX: Ideal gas law
    is molar mass
Continuum Assumption
Fluid molecules aren’t confined to a lattice, and move around, so how do we deal with a volume in which the number of particles is constantly changing?
  Only at extremely small sizes this makes a difference, so we can assume that values vary continuously through space (Continuum)
Material Classification
Materials can be classified based on how they respond to a shear force
In this class, we will only be focusing on Newtonian and Non-Newtonian fluids
  Newtonian fluids have a constant viscosity, while Non-Newtonian fluids have viscosities that change

## Slide 7
Transport Properties
Viscosity – resistance to flow
Couette Flow (drag flow)
Liquid between and stationary and moving plate in which flow is being caused by the moving plate
Assumptions
  No slip at the boundaries
  The fluid is moving at the same speed as the moving plate at the boundary
Observations
  Velocity () changes from 0 at the stationary plate to the velocity of the top plate () at the top
  The height () is small, and this makes velocity () vary linearly in the y direction
    This is the case for most fluids
  Example of laminar flow
    Horizontal streamlines (lines depicting fluid movement where the velocity is constant along the line)
  Motion of one layer of fluid “pulls” the others along with it due to molecular friction
    Local shear stress () is linearly related with the velocity gradient ()
      Shear stress is from the surface in the y direction due to flow in the x direction
      Newton’s law of viscosity (1687):
        For Newtonian fluids, viscosity is represented as
        Non-Newtonian fluids have a viscosity which is a function of
    Like moving a deck of cards between a table and one of your hands
Viscosity
  A quantity expressing the magnitude of internal friction in a fluid resisting flow, in which parallel fluid layers move relative to each other, interact, and transfer momentum between them
  How does this happen in different types of matter?
    In liquids, this occurs because of the constant breaking and reforming of interactions between molecules
      As temperature goes up, the interactions get weaker, and viscosity goes down
    In gases, this occurs because of the random motion of molecules causing collisions
      As temperature goes up, more collisions happen, and viscosity goes up

## Slide 8
  How is viscosity measured?
    By how it responds to a simple deformation, where only one component of velocity is non-zero
    Most often this is in the form of simple shear flow
      The two types of simple shear flow are Couette flow and Poiseuille flow (pressure driven through a pipe)
    Using Couette flow (Rotational viscometer/rheometer)
      Fluid trapped between stationary rotating surfaces
      Torque related to the viscosity of the fluid
    Using Poiseuille Flow (Capillary viscometer/rheometer)
      Fluid forced through a circular tube
      Pressure related to viscosity

## Slide 9
Finding Shear Stress
Found through manipulating Newton’s Law of viscosity
Another way: Using (Shear Strain)
At the point where the fluid is in contact with the moving plate
If is small:
So…
Often called the Shear Rate
Poiseuille Flow (pressure-driven flow)
(Quick detour)
No moving plates
  Velocities at the plates are still 0 because of the no-slip assumption
Instead of a linear velocity gradient, it is parabolic

## Slide 10
Determining viscosity with Viscometers
More Units
Determining Units for Viscosity using Newton’s Law of viscosity :
has units of
has units of
So, has units of
Concentric Cylinder:
Known radii (), height (), angular speed (), torque ()
Moment arm here is the distance from the toque shaft to the end of the cylinder ()
: Shear stress from surface in the direction due to flow in direction
Substituting and rearranging…
Remember: only valid for small gaps

## Slide 11
Cone and Plate (More commonly used)
So, the shear rate is uniform throughout the fluid
Viscosity for Non-Newtonian Fluids
Alpha is usually smaller than . Usually around