## Slide 1
Course Info
Time: TR 8:00-9:15 AM
Location: CHEN 106
Instructor: Jeetain Mittal
Office: CHEN 500
Phone: (979) 862-1920
Email: Jeetain@tamu.edu
Office Hours:
  Monday 2:00-3:00 PM
  By appointment
Teaching Assistants:
Reagan Kutter
  Email: regankk@tamu.edu
  Time: Friday 1:45-2:45 PM
  Location: CHEN 340
Ashish Shyam Tangade
  Email: ashish.tangade@tamu.edu
  Time: Wednesday 4:00-5:00 PM
  Location: CHEN 340
Category | Date | Percentage
Participation/Quizzes | N/A | 5%
Homework | N/A | 10%
Midterm 1 | Sep 24th | 25%
Midterm 2 | Nov 7th | 25%
Final | Dec 6th 1:00-3:00 | 35%
Grading Info

## Slide 2
1st Law of Thermodynamics: Energy is conserved
Energy Balance on closed system
Enthalpy
Energy Balance on open system

## Slide 3
Finding Temperature through changes in enthalpy
Constant Volume and constant Pressure heat capacity
Temperature Dependence on heat capacity

## Slide 4
Equations of State
Gibbs’ Phase Rule
π = Number of phases, N = number of species
Ideal Gas Law
Finding Q, W, U, and H for reversible, closed systems

## Slide 5
Real Gasses
Van der Waals Equation of state
Virial equation
Cubic Equations of state

## Slide 6
Pitzer Correlations
Compressibility Factor
Second virial coefficient
To find the values and , use the tables in appendix D.
The Pitzer correlation for the second virial coefficient can only be used if inside the dotted line in on the figure below
Note: Ideal gas law is acceptable to use if is between 0.98 and 1.02 (2% error)
Generalized correlations for liquids
Rackett equation
Two parameter corresponding states
  Use density with the chart to get other info
Good For saturated liquids
Changes in states for liquids based on isothermal compressibility and volume expansivity:

## Slide 7
Entropy
2nd law: energy has different amounts of quality
EX: Work is more useful than heat

## Slide 8
Changes in entropy of an ideal gas
Changes in entropy of an ideal gas in an open system
Chapter 6
Internal Energy
Enthalpy
Gibbs Free Energy
Helmholtz Free Energy

## Slide 9
Internal Energy
Maxwell’s Relations
Enthalpy
Gibbs Free Energy
Helmholtz Free Energy
Other Relations to keep in mind

## Slide 10
Residual Properties
Residual = Actual - Ideal
Using second virial generalized correlation
Note: this method can only be used if you are inside the line on the figure below
Using Lee Kesler Tables
Values can be found in appendix D

## Slide 11
Introduction
Equilibrium
State of balance, no unbalanced driving forces
Thermal EQ: Uniform temperature
Mechanical EQ: Uniform pressure to no tendency for pressure to change locally
Phase EQ: Mass of each phase stays in the same quantity
Chemical EQ: No tendency for changes in chemical composition
Thermodynamic EQ: Equilibrium with respect to all possible changes in state
To be at equilibrium, the system must be
isolated (No exchange of energy, mass or
volume). Entropy must also be at a maximum.
Internal energy will be at a minimum
Process: any change that a system undergoes
from one state to another
Path: The series of states a system
goes through during the process
To fully describe a process, one must know the
initial and final states, as well as the path taken
New way to define internal energy:
<- inexact differential
(used for path functions)
From Themo I
New Term associated with chemical potential
If n=1
The fundamental equation

## Slide 12
U(S, V, n)
Expressing thermodynamic properties in terms of different variables
Helmholtz Free Energy
Enthalpy
Gibbs Free Energy
Entropy
Internal Energy
Helmholtz and Gibbs are the most useful, because they are expressed in easily found values
All the energies are at a minimum at equilibrium, and entropy is at a maximum
Why didn’t we need the chemical equilibrium term before now?
Before this we were dealing with single phase closed PVT systems, so
For a system in which there are two phases and N number of species, can be applied separately to each phase
Combining them,

## Slide 13
This means that
Since the changes in one phase are equal but opposite to the other phase
The differentials are independent and arbitrary, so the only way this equation is satisfied is if:
= 0
So, at equilibrium, the chemical potential for each phase of a species is equal

## Slide 14
Chapter 10 & 11: Solution Thermodynamics
Mass/mole fractions
Molar concentration
10 is composed of a bunch of math, while 11 is applying it. Here we are combining them to hopefully make it easier
How do we use pure component properties to predict mixture properties?
You can’t simply get properties of mixtures by adding the pure property components together
Intensive form for the difference between the actual volume and predicted volume
: ideal solution, : contraction, : expansion
In general,
Where M is V, S, U, H, A, or G
If we define as and as , we get
is the excess property
For entropy we need to add another term
This is because adding 2 of the same species together will increase the entropy
This applies to functions with entropy as well,

## Slide 15
Mathematical framework for solving for solutions
Partial Properties: Represent the actual change from the expected property when in a mixture
How the actual property changes with respect to the amount of it in the mixture with everything else held constant
These can be hard to represent, because The relationship can change in different ways depending on other factors.
Quantities of other substances
Representing a change in a property based on the changes of its dependent variables (using a two-substance mixture for simplicity)
Can be represented as partials
Combining all these equations ans inserting partials…
Consolidating terms into and camps