## Slide 1
Course Info
Time: MWF 9:10-10:00 AM
Location: CHEN 106
Instructor: Hung-Jen Wu
Office: CHEN 227
Phone: (979) 862-1454
Email: hjwu@tamu.edu
Office Hours
  MW 10:00-11:00 AM
  By appointment
Message brought to you by Python gang
Teaching Assistant: Beth Wei
Office: TBA
Email: bettywey@tamu.edu
Office Hours
  TBA
Category | Date | Percentage
Practice Quizzes | N/A | 15%
Pop Quizzes | N/A | 5%
Homework | N/A | 15%
Midterm 1 | Sep 27th | 20%
Midterm 2 | Nov 13th | 20%
Final | Dec 6th 8:00-10:00 | 20%
Reflection Letter | TBA | 5%

## Slide 3
Issues for computational methods
Convergence
  The way we try to solve problems is through iterations, so we must make an initial guess to solve it. If the guess doesn’t work out, we must make another guess. A good numerical method will converge to the answer we want.
Accuracy
  The answers we get must be correct. Usually expressed by the number of significant digits
Stability
  Like convergence, but for differential equations, stability has a different meaning. Will be covered when we get there
Computational Efficiency
  Most questions are simple in this course, but large-scale simulations can cause issues, so efficiency is necessary.
Chapter 1: Introduction
Example Problem:
A numerical analysis solution could test points what you give it, and from there, find the answer.
Numerical Error
Total error: difference between the true value and the numerical approximation.
Relative error: Total error over the exact answer
These are not practical, because would you find the numerical approximation, if you already know the answer?
Truncation errors: Difference between the exact value and the power/Taylor series expansion with a finite number of terms

## Slide 4
Computer related stuff
Round-Off Error: comes form computer itself
Computers can only hold a certain number of digits
Digits left off by the computer are called round off errors.
Round off error can make a significant impact when subtracting two very close numbers
Precision (floating point format)
Single (32 bits): ~7 sig digits
Double (64 bits): ~15 sig digits
MATLAB uses double by default, so to get single, you will have to specify
Triple precision is possible with 128 bits
Suppose your computer can only hold 3 sig digits
Cancellation error: comes when there is a massive difference between the expected and calculated answers
EX: consider a situation when your square root function only goes to 4 digits
One solution is only off by 0.04%, but due to a cancelation error, the other one is off by 100%
You can reformulate the equation to get a better answer
This may not be very useful now because most function in the computer have a higher accuracy, but later, for differential equations, this becomes more useful

## Slide 5
Matrix Operations
Matrix Equality: (A = B) means that A and B have the same number of columns and rows, and the values in the same positions are the same
Matrix Addition: (A + B = C) means that A and B had the same numbers or rows and columns, and C is the values in the same positions in A and B added together
Matrix Multiplication: The element in the resulting matrix is found by doing the scalar product for the values in the original matrices of the same column and row.
The first matrix should have as many rows as the second has columns
Fundamental mathematics to know: Vectors and Matrices
A matrix is characterized by the number of rows and columns it has. Rows are the horizontal elements and columns are the vertical elements.
General matrix with m rows and n columns

## Slide 6
Chapter 2: MATLAB
Variables
Can store numbers, strings or unknown quantities
Variable names operate like python, assignments are like python as well
Globally defined
Floats are double by default
Operators
‘+’ addition
‘-’ subtraction
‘*’ multiplication
‘/’ division
‘^’ exponentiation
Syntax special variables
‘ans’ used to store the result of an expression
‘clock’ variable that contains the current time
‘date’ contains the current day
‘i’ sqrt(-1)
‘Inf’ when a number exceeds the maximum or minimum number
  >1.7E308 or <-1.7E308
‘j’ sqrt(-1)
‘NaN’ stands for not a number
  Usually, the result of an undefined math operation (0/0 or log(-2))
‘pi’ pi to 15 sig digits

## Slide 7
Use a semicolon at the end of a line to prevent it from printing on the command line
Use ‘%’ to comment
Use ‘%%’ to designate sections
Some Tips

## Slide 8
Matrices and Vectors
Creating vectors
Creating a row vector: v = [1, 2, 3]
Creating a column vector: v=[1; 2; 3]
Creating a larger vector:
  v = [start:step:stop]
    The stop is inclusive
  v = Linspace(start, stop, # of indices)
Transposing Vectors
v = v’
v = transpose(v)
Some Vector info
Get a certain value from a vector
  v(index)
    Indices start at 1, not 0
Max and min
  [value, index] = max(v)
  [value, index] = min(v)
Length
  v_length = length(v)
Creating Matrices
M = [1, 2, 3; 4, 5, 6]
  To make matrices easier to read in the code, use ‘…’ after the row, and proceed to the next row. This will make it, so your matrix looks as it functions in the code.
You can also create them by using vector variables
  M = [r1; r2; r3]
Or you can make them with a collection of columns
  M = [c1, c2, c3]
Vector with sequences:
  M = [start:step:stop; …]
Vector with all 1’s or 0’s
  M = ones(height, width)
  M = zeros(height, width)
Identity matrix
  M = eye(size)
Accessing info from matrices
M(row, column)
Retrieving a row or column
  M(row, :)
  M(:, column)
Getting the size of a matrix
  result = size(M)
    Given as ‘rows columns’
Transposing Matrices
  Same as Vectors
Max and min of matrices
  You need to take the max / min twice to get the actual maximum/minimum of the matrix twice
  max_val = max(max(matrix))

## Slide 9
Cell Arrays
Can hold any data type and data in the cells can differ in type
Like a list of lists from python
Useful Applications:
  When you have many instances of a similar structure of data
    EX: you have 100 reactors and don’t want to individually define all of them
Creating Cell Arrays
  cell_array{row, column} = (any type of data)
Structured Arrays
Organize data and access it by name
Like a cell array but the second dimension is not just an integer, but a way to name the data
Like a python dictionary

## Slide 10
Common Operations
Importing Data:
  csvread: reads a csv file
  M = csvread(filename)
  We will mainly use this function for importing data
  xlsread: reads excel file
  Don’t use this, it works for older spreadsheets
  readcell: new version for reading excel file
Dot Operations:
  Allows you to combine two matrices in a variety of ways
  ‘.*’ will multiply the elements of two matrices together
  ‘./’ will divide the elements of the first matrix by the second matrix
  ‘.^’ will raise the elements of the first matrix by the second matrix
  All these work with scalars

## Slide 11
Logic
If Else Statements:
If condition
  Code to execute
elseif condition
Code to execute
else
  Code to execute
end
break and continue are available for loops
Output
Copying values from MATLAB into excel is possible
  Just open the spreadsheet menu and copy and paste
  Also, downloading .mat files for a single variable or all variables in your workspace is possible
fprintf(formatted string)
  Can use this to format your outputs (like an f string)
    Can put multiple variables in a string
  Use ‘\n’ to jump to the next line
While Loops
while condition
code
end
For loops
for iterable
code
end
  Iterables take the form i = start:step:stop

## Slide 12
m-files
Used for creating functions\
Anonymous functions (Lambda functions)
  Takes the form: function_name = @(var1, var2…) function
Actual functions as files
  Functions can have multiple outputs. To take advantage of this, use a vector [var1, var2]
  Useful for large amounts of code
Plotting
plot(x, y) creates quick, dirty plots
Some formatting can easily be applied to make your plots better

## Slide 13
Plot formatting
  plotted_data = plot(x_data, y_data)
    To put multiple data sets on a plot, use ‘hold on’ after the first one
  set(plotted_data, ‘Color’, [R, G, B]) The RGB values are normalized to 1
  set(plotted_data, ‘LineStyle’, ‘-’)
  to change bounds
    xlim([start, stop])
    ylim([start, stop])
  to change axis labels
    xlabel(‘name’, ‘FontSize’, int)
    xlabel(‘name’, ‘FontSize’, int)
  Title:
    title(‘title’, ‘FontSize’, int)
  Legend:
    Legend(‘name for first graphed data’, …)
Symbolic Toolbox
defining symbolic variables
  syms var
To do fractional math without decimal points
  sym(frac)
Simplify functions
  expand(sym_func)
  simplify(sym_func)
substitute values in a symbolic function
  subs(sym_func, [var1, var2, …], [val1, val2, …])
Factor polynomials
  factor(sym_func)
Convert to anonymous function
  matlabFunction(sym_func)
Derivatives/Integrals
  diff(sym_func, var, order)
  int(sym_func, var): indefinite
  int(sym_func, var, from, to) definite
    can use symbolic variables for form and to
  What if your integral has no easy solution?
    vpa(integral)
These functions do not change the existing variable, make sure to assign new variables when making them

## Slide 14
Some other functions that are useful
lower(str) -> returns the string but in all lowercase
error(message) -> raises an error

## Slide 15
Chapter 3: Single Variable Nonlinear Equations
Ideal Gas law is an example of a nonlinear equation
First way of solving a single nonlinear equation:
In this example, the Van Der Waals equation of state was manipulated to be equal to zero. Now you can solve for the needed variable through trial and error
This way is not very efficient for solving these types of problems
Also, this cannot be solved for equation
For iterative solutions:
When finding out when to terminate an iterative solution, a test needs to be applied
Normally, the relative change is used:
For solutions near zero, a different criteria is used:
Note: use the x value, not the value of the function for the ahead methods
Newton’s Method
Uses Truncated Taylor series expansion after 2 terms to find the next term
Solves for where f(x) = 0
If multiple roots exist, the slope determines which one will be found. You will have to use multiple starting points
Sometimes your answer will converge, other times it will diverge. It depends on what the character of the graph looks like and what starting point you choose

## Slide 16
Converging
Example
Diverging
Example
For this equation, Newton’s method can’t be used

## Slide 17
Secant Method
Instead of finding f’(x), we will use the finite difference
Good for equations that have if statements (piecewise)
Need two guesses, but you can just choose one close to your first
Bounding Method
Preferable to Newton’s method for solving single variable nonlinear equations
Three major bounding methods:
  Bisection method
  Regula False method
  Illinois method
Only doesn’t work when the point passes through zero but doesn’t cross into the other side of the axis EX: f(x) = x2

## Slide 18
Bisection Method
Once an a and b are found such that the root is in between them, the midpoint is found and calculated
P replaces whichever point had the same sign as f(p)
P would replace b in this instance
For this method, error would be the difference between the two points
Regula Falsi Method
The next point is found by applied based on the secant method
Slow convergence for highly nonlinear functions
Illinois Method
Modification of the Regula Falsi method
Follows the Regula Falsi method, except when
Then they use
The fzero function in MATLAB uses a mix of the bisection and Illinois method

## Slide 19
MATLAB Function - fzero
Syntax:
x = fzero(f, x0, options)
  f is the function handle (anonymous function or function file)
    When using a function file, you must put @ before the name
  x0 is the initial guess
    Only one guess because the computer find the other one
      Sometimes you can find issues with this where the search for a second x will cross 2 solutions at once, but the computer has no idea it did that
    another option is to send in a vector with custom bounding
      EX: [lower_bound, upper_bound]
  Options are some manual settings you can set
    Ex: options = optimset(‘’TolX’, tolerance, ‘Display, ‘iter’)
      tolerance must be set in scientific notation in the form {num}e{int}
      ‘iter’ will display the number of iterations
  x is the solution
Has a relative convergence criteria of 10^-6, which usually provides 5 sig figs of accuracy
Solve function (symbolic)
Same built in tolerance as fzero
When outputting, make sure to convert to a float by using the double(value) or vpa(value) function
Will locate all roots, so no starting point is needed
Syntax:
x = solve(symbolic function, symbolic variable)
  If you want to set the function equal to something, use ==
When solving these types of problems (Chap 3), If you have an opportunity to reformulate an equation so you don’t have your variable in the denominator, Do it

## Slide 20
Chapter 4: Systems of linear equations
Takes the form
x is a column vector with the number of variables
B is a column vector with all the solutions
A is a square matrix with one side having the
same length as the x and B column vectors
(also referred to as the coefficient matrix)
For these problems, round off error will impact the accuracy of the answers
For large problems, computational efficiency is key
Gaussian Elimination
This is the classic way of solving these types of problems. There are two steps:
1. Forward elimination where a variable is eliminated until there is only one remaining
2. Backwards substitution where you go back through the equations to find the value for each variable
(Round off error can come into effect during this part of the problem solving because with large systems, they can stack on one another when going backwards)
For systems of linear equations, there are two cases. One where all the equations generated by the matrix multiplication are independent (non-singular), and one were some or all the equations are dependent on each other (singular)
There’s no solution for singular systems

## Slide 21
Problems with Gaussian Elimination
1. cannot eliminate an unknown:
You cannot eliminate x1 with the first equation because the coefficient is 0
This problem is easily solved by row pivoting (switching order of equations)
MATLAB has a built-in function ‘\’ to solve this issue
2. Ill conditioning
sometimes there is a large overlap in uncertainties when solving for a variable
This happens when the slopes approach each other slowly.
This amplifies the round-off-error (the main problem)
Another issue with Ill Conditioning:
When eliminating, you can have problems when equations have completely different magnitudes
This can be solved by scaling, which is multiplying the equation by a constant to make them similar in magnitude
you have to do this on your own

## Slide 22
MATLAB functions for linear systems of equations
A banded Matrix has many 0’s and leads to easier solving, but computers can have issues with it. This function doesn’t have an issue with it
LU decomposition
Benefits:
after finding L^-1B,
you can start backwards
substituting immediately
useful for when the B
vector varies but A remains
the same (not as a function,
but you must use A to solve multiple different B’s)
Reduces computation and increases speed, but not necessary if your computer is good enough

## Slide 23
Condition Number – can be used to determine ill conditioning
Gauss-Seidel Method
Gauss-Seidel is good for computer efficiency, but likely not needed in our case

## Slide 24
0 is the initial guess
Solving linear equation with symbolic toolbox
solve function
  Just enter the equations separated by commas
  Solve(eq1(x1,x2,x3), eq2(x1,x2,x3), eq3(x1,x2,x3), x1, x2, x3)
  You can use unspecified constants that are symbolic variables
    What this function is the most useful for
Takes significantly more computing power than backslash

## Slide 25
Chapter 5: Systems of nonlinear equations
Bounding method doesn’t work, so we need to use Newton’s method. (also, secant method doesn’t work)
In addition, plotting a function will not be able to help you solve a solution
Example of a system of nonlinear equations
This one can be graphed, but more complex systems won’t be able to.
Numerical way of solving systems of equations
Newtons method is based off Taylor Series, so let's review that

## Slide 26
For our purposes, we will be using the first term of the Taylor series expansion
Developing our solution
We are going to use this as an example
First, we must make an estimation (let’s say x1 = 4 and x2 = 2)
Using the first term of the Taylor series expansion

## Slide 27
Because f1 and f2 = 0
Now, we solve this system on non-linear equations
Now repeat at these new x values until convergence
This is Newton’s method for a k amount of equations
A matrix
(Your partial derivatives at your previous x values)
Also known as the Jacobian
x matrix
b matrix
(the values of your functions at the previous x values multiplied by negative one)

## Slide 28
Your A matrix is also known as the Jacobian
You can find the equation using the symbolic toolbox
Your functions
The values of these variables to find the Jacobian at
The built in Newton’s Method function (fsolve) uses finite difference to find the Jacobian
Some notes on Newton’s Method:
Can solve 95% of nonlinear systems of equations
A good initial guess is usually required for reliable convergence
  Some systems have multiple solutions, and you need to choose an initial condition close to the solution you want
The more linear the system is the easier the solutions can be found
  Polynomials are counted as close, logs and exponentials are not
    Usually, we will have to reformulate equations with logs and exponentials
Luckily for us, we don’t need to do any of this (except find initial condition)
To get the MATLAB function version of your Jacobean (this is useful because the Jacobian gives a symbolic solution) use:
your_func = matlabFunction(symbolic_eq)
  This returns an anonymous function

## Slide 29
fsolve – newtons method function
Very similar to the fzero function
The ‘@fx’ is a column vector consisting of the functions
The variable ‘x’ is a vector as well. In the function you will call the ‘ith’ value of the variable for each one.
  EX f = [x(1)^2 + x(2)^2 - 5 36; x(1)^2 – 3*x(2) – 16]
x0 is a column vector of guesses for each variable
You will want to reformulate your equations if you have variables in the denominator of functions (the example below needs to be reformulated)
The fval variable is a column consisting of the values that the formulas evaluate to at the found solution
In this example, some variables are set as x(i) for simplicity and readability

## Slide 30
Tearing method
Useful when dealing with a single highly nonlinear equation (exp or log).
The idea is that you guess a value for one of the x values, then you solve for the other values using the more linear equations. Then you would check to see if that last equation is consistent.
Part one would be using fsolve, and part two would be using fzero.
Say we have this system of equations
Base line analysis
Solving for x and y in these equations is relatively simple, since there are two equations with just them and x
First method (not as useful, but mainly for showing an example)
Now, by subbing these values into equation one, we can solve with fzero
Advantages to this method
Finding an initial guess is much easier
The solution is more stable
Disadvantage
If we had another term with variables in equation 2 or 3, that would made this way impossible
2nd method (more practical)
Guess an x value, then solve equation 1 and 3 for z and y using fsolve
Then check equation 2 to see if it equals 0
Use fzero to find an x value that satisfies that eq 2 equals 0
This method can be used for a wider variety of problems because fsolve is more versatile than solving by hand

## Slide 31
The gz function gives the value of equation 2 at the current guess of x
  Use fsolve to find the remaining variables at the current guess of x
    The initial condition doesn’t matter, because for a linear system of equations, Newton’s method will always approach the answer
Like with chapter 3, it would be a good idea to now graph the equation to get a good initial condition
  We see two zeros, so we will solve for both
Now we use the fzero function to find the x values
Now we must go back and use fsolve to locate the other variables
  To get a good initial guess for y and z, you will probably have to play around with the function a bit

## Slide 32
Chapter 6: Polynomial Approximations
Overview: Use polynomial approximations for
  Derivatives
  Interpolation
  Integration
Used for when we just have a ton of data points
Derivatives – finite differences
Comes from Taylor series
To find f’(x), we use a first order approximation (only go until you get to the first derivative term)
The rest is the error

## Slide 33
Second order approximations (More accurate):
Central difference approximations
Ignore the rest
Technically a second order approximation, so more accurate
You can also add the 2 equations together to get the second derivative
The central difference approximation is great and all, but to get it, you must narrow your data by one, because the first and last terms don’t have surrounding data points. So, how can we find approximations for those?

## Slide 34
Second order terms for forward and backwards
Error
Central difference is good for the middle data points. Forward and backward are good for the first and last points respectively.

## Slide 35
An example for center difference approximation with unequal spacing
Cross-outs are error
Interpolation
Linear
You know it, you love it
Quadratic
Don’t use polynomial approximations greater than 2nd order (what we have here)
Use backslash to find a, b, and c
Generally better than linear interpolation

## Slide 36
Spline function
Using 3rd order quadratic vs Spline function
How it works – Quadratic Spline
Spline passes through each data point
Each segment between data points has its own cubic function
The first derivatives of the spline must be equal upon intersection
The first spline is linear
How to make the equations
For N + 1 points, there are N segments. Each segment has 3 unknown variables, so there are 3N unknowns and you need 3N equations
2N equations come from the boundaries of the functions, where the equation equals the data point
N – 1 data points come from setting the 1st derivatives equal
1 equation comes from setting the coefficient in the first equation associated with the quadratic polynomial equal to 0
Use \ to find your coefficients
You can also use this for differentiation and integration. The answers you get from the spline function are probably more accurate than the finite differences before this and integral approximations later in the chapter.

## Slide 37
Cubic Spline
This method is more common, since we already have quadratic interpolations, which does similar things to the spline function on the previous page
How it Works:
Approximation passes through all data points
Each segment has its own cubic equation
The first and second derivatives a must be equal upon intersection
The second derivative is zero at both points
spline function
fv = spline(xd, fd, xv)
  fv is the interpolated values based on xv (vector or number)
  xd are the x values
  fd are the f(x) values
  xv are the values for interpolation (vector or number)
  If you don’t pass in interpolation values, you will get back details about the functions

## Slide 38
Integration:
Trapezoids
MATLAB function:
A = trapz(x, f)
A is the integral
x is the x values
f is the function values
Simpson’s Rule
Quadratic interpolation, then integrate
Requires an odd number of equally spaced data
More accurate than the trapezoids, but harder to apply due to restrictions
Simpson’s rule for 3 data points
General Simpson’s rule formula
n is even (starts at 0, so you have an odd number of data points)

## Slide 39
Chapter 7: Initial Value ODEs
The symbolic toolbox has a function to solve ODEs, but it’s unreliable
Two types of problems:
Initial value problems
  When the initial condition is given at the same ‘x’ or ‘t’ value
Boundary problems
  When the initial condition is given at different ‘x’ or ‘t’ values
In the differential equations class, we didn’t care, but for numerical methods these two types of problems are solved in different ways. Boundary condition ODEs are covered in chapter 8.
(y terms are linear)
(Have x or t values in front of y)
(y terms squared or some other function)
(Have x or t values in front of y)
RHS = 0
For ODEs, you need as many initial conditions as the order of your differential equation.
For linear equations, the conditions can either be initial value or boundary
To have one solution for nonlinear ODEs, the conditions must be initial value
  If you have a boundary problem, you don’t know until you solve

## Slide 40
dsolve
To make differential equations in MATLAB, we need to use the diff function
Your function
Constants
Derivatives of your function
The differential function
What your differential function equals
Setting your constants equal to whatever
You can use vpa to then give your coefficients in decimal form
This indicates the number of decimal places to show
Keep in mind dsolve only works for simple differential equations
Using dsolve with initial and boundary conditions
Giving your differentials variables so you can set them equal to something in the dsolve function
Problems dsolve can solve

## Slide 41
Explicit Euler’s Method
for first order differential equations
General form for first order ODE
Very simple. Just calculating the next value of y based on the previous one
Local truncation error is O(x^2)
The MATLAB function finds this by just calculating the local truncation error rather than finding the actual error (exact value – numerical value)
Use low step size for better accuracy
Euler’s method is not extremely accurate, but it is quick and simple
Runge-Kutta Methods (Higher order than Euler)
Can achieve the accuracy of a higher order approach without requiring the calculation of higher derivatives
2nd Order
4th Order (most common)
Explicit Methods
When starting a question, 4th order RK is usually a good place to start

## Slide 42
Implicit Methods
Implicit Euler’s
These are more stable than explicit methods
You may have to solve for the y+1 term using fzero because it might be a single variable non-linear problem
Trapezoidal Method
You must use fzero if f is nonlinear with respect to y
More accurate than the Euler’s method because this is higher order
With these methods, using the previous y value as a guess for the fzero function should be sufficient
Backward Difference Method
Comes from finite differences
You need two initial conditions, or you can find the 2nd term using the Euler or Trapezoidal method, then use Backward Difference
Systems of ODEs
For these types of problems, instead of just being given differential equations of multiple functions
For explicit methods, you should have no problem. For implicit methods, you might have to use the backslash or fsolve function to find the solution

## Slide 43
Higher order ODEs
Convert into system of ODEs
Converting higher order ODEs to systems is necessary when using the built in functions
Just rearrange the function given into terms of the higher order, then just say the derivative of the lower order ones are the next higher up derivative